## Slide 1: A Two-Pass Algorithm for Automatic Loudness Correction
Alexey Lukin, Russell McClellan, Aaron Wishnick
iZotope Inc., Cambridge, MA
Convention paper 9683
141st AES Convention
Sept 29 – October 2, 2016
Los Angeles, CA

## Slide 2: Level measurements
Traditional way: sample peak, RMS

## Slide 3: Level measurements
Traditional way: sample peak, RMS
New way: true peak, loudness (BS.1770)

## Slide 4: Level measurements
Traditional way: sample peak, RMS
New way (BS.1770): true peak, loudness
  Integrated (programme) loudness
  Short-term and Momentary loudness

## Slide 5: Level measurements
Traditional way: sample peak, RMS
New way (BS.1770): true peak, loudness
  Integrated (programme) loudness
  Short-term and Momentary loudness

## Slide 6: True peaks
Part 1

## Slide 7: True peaks
BS.1770 upsampling filter
±0.1 dB
Equiripple filter design has ripples in both passband and stopband, can underestimate peak levels

## Slide 8: True peaks
Aliased (real-use) frequency response
Aliasing in measured levels created by sampling of 4× upsampled signal

## Slide 9: True peaks
Improved filter design
  Reduced ripple

## Slide 10: True peaks
Improved filter design
  Reduced ripple
  Peak finding by cubic interpolation

## Slide 11: True peaks
Improved filter design
  Reduced ripple
  Peak finding by cubic interpolation
  Also using sample peak levels

## Slide 12: True peaks
Improved filter design
Aliased frequency response during practical use

## Slide 13: True peaks
Improved filter design
Aliased frequency response during practical use
*
__________________________
* Is not compatible with the baseline BS.1770 upsampling filter

## Slide 14: True peaks
Our solution:
Aliased frequency response during practical use

## Slide 15: Loudness correction algorithm
Part 2

## Slide 16: Loudness correction
Flowchart of loudness correction
  Fixed gain to correct Integrated loudness
  Dynamic range compression for limiting Short-term/Momentary loudness (optional)
  True peak limiting
Gain
(integrated)
Compression (short-term/momentary)
Limiting (true peaks)

## Slide 17: Loudness correction
  Easy to implement, single-pass operation
  Each stage of correction affects the result of other stages, e.g.: limiting changes the Integrated loudness
Gain
(integrated)
Compression (short-term/momentary)
Limiting (true peaks)
+
–

## Slide 18: Loudness correction
Challenge: find the amount of gain G which achieves the required Integrated loudness, in anticipation of limiting
Gain
(integrated)
Compression (short-term/momentary)
Limiting (true peaks)

## Slide 19: Loudness correction
Step 1: create the histogram of peak levels from the limiter envelope
level, dB
popularity

## Slide 20: Loudness correction
Step 1: create the histogram of peak levels from the limiter envelope
level, dB
popularity
True peak limiter threshold

## Slide 21: Loudness correction
Step 1: create the histogram of peak levels from the limiter envelope
level, dB
popularity
True peak limiter threshold
Expected duration of limiter activity

## Slide 22: Loudness correction
Step 2: create the histogram of momentary loudness
loudness, LKFS
popularity

## Slide 23: Loudness correction
Step 2: create the histogram of momentary loudness
loudness, LKFS
popularity
Translate the limiter threshold
Expected duration of limiter activity

## Slide 24: Loudness correction
Step 3: “clip” the histogram to predict the effect of peak limiting on loudness
loudness, LKFS
popularity

## Slide 25: Loudness correction
Step 4: recalculate Integrated loudness from the updated histogram
loudness, LKFS
popularity

## Slide 26: Loudness correction
Step 5: update the required gain G and go to step 2

## Slide 27: Loudness correction
Step 5: update the required gain G and go to step 2
This iterative process updates the histogram of momentary loudness based on the expected amount of peak (and loudness) limiting until it converges on the required amount of gain G

## Slide 28: Loudness correction
Once the gain G is determined, the whole processing chain is ready to be applied
Gain
(integrated)
Compression (short-term/momentary)
Limiting (true peaks)

## Slide 29: Loudness correction
Once the gain G is determined, the whole processing chain is ready to be applied
Integrated loudness of the output may not exactly match the prediction
Gain
(integrated)
Compression (short-term/momentary)
Limiting (true peaks)

## Slide 30: Evaluation
Tested products:
  iZotope RX Loudness Control,
  Nugen LM-Correct 2,
  Minnetonka AudioTools Focus for Loudness Control,
  iZotope RX (Loudness module),
  TC Electronic LC2n Loudness Correct,
  RTW CLC (Continuous Loudness Control)

## Slide 31: Evaluation
Test conditions
  A collection of 6 audio samples with wide dynamic range and diverse genres
  Each sample processed with 3 sets of loudness targets:

## Slide 32: Evaluation
True peak compliance

## Slide 33: Evaluation
Integrated loudness compliance

## Slide 34: Evaluation
Short-term/momentary loudness compliance

## Slide 35: Results
Improved accuracy of Integrated loudness – best in class of non-iterative methods
Spot-on True peak and Short-term loudness

## Slide 36: Results
CPU performance

## Slide 37: Summary
Loudness correction cannot be done accurately in realtime: all targets are interrelated

## Slide 38: Summary
Loudness correction cannot be done accurately in realtime: all targets are interrelated
2-pass (analyze/correct) software struggles to achieve accurate Integrated loudness

## Slide 39: Summary
Loudness correction cannot be done accurately in realtime: all targets are interrelated
2-pass (analyze/correct) software struggles to achieve accurate Integrated loudness
The proposed method shows an improved precision

## Slide 40: Your questions
?